## Slide 1: Can FPGAs accelerate your workload?
Mike Kinsner, Principal Engineer @ Intel

## Slide 2: 1) Mapping an Algorithm to Hardware
A framework for thinking about Field Programmable Gate Arrays (FPGAs)

## Slide 3: Data Flow Graph: The Core of Modern Compilers
for (int i=1; i < 10; ++i) {
A[i] += B[i-1] * 5;
}
load
load
store
5

## Slide 4: Data Flow Graph: The Core of Modern Compilers
for (int i=1; i < 10; ++i) {
A[i] += B[i-1] * 5;
}
Hardware?
load
load
store
5

## Slide 5: Executing in Silicon: Two key options
Option 2:
Materialize data flow graph directly on reconfigurable spatial hardware
Option 1:
Instruction set architecture (ISA) machine
for (int i=1; i < 10; ++i) {
A[i] += B[i-1] * 5;
}
Execute consecutive instructions on same hardware via time multiplexing
Execute instructions on different hardware by specializing device regions in pipeline
Register file
Data memory
Instruction memory
ALU
load
load
store
5
Hardware with configurable spatial “regions”
IP

## Slide 6: Many Architectural Tradeoffs
Spatial Architecture
Materialize data flow graph directly on reconfigurable spatial hardware
Instruction Set Architecture
for (int i=1; i < 10; ++i) {
A[i] += B[i-1] * 5;
}
Register file
Data memory
Instruction memory
ALU
load
load
store
5
Hardware with configurable spatial “regions”
+ Excellent Perf, Perf/Watt from specialization
- Historically inaccessible by SW developers
- Data path not typically runtime context switched
+ Easy to program
+ General purpose at runtime
- Not all hardware may be used every clock cycle
IP

## Slide 7: Think of as a Reconfigurable Custom Chip
Spatial Architecture
Register file
Data memory
Instruction memory
ALU
load
load
store
5
Reconfigurable Spatial (e.g. FPGA)
IP
Fixed Spatial (e.g. ASIC)
Think of FPGA as able to implement what you would build as a custom data path on a dedicated chip/ASIC!
(there is an overhead cost to FPGA reconfigurability vs ASIC, but much less expensive in low/medium volumes and reconfigurable)

## Slide 8: 2) Field Programmable Gate Arrays (FPGAs)

## Slide 9: What is a Modern FPGA?
Massive array of small processing units
  1-bit ALUs (~millions)
  Dual-ported memories (~ten thousand)
  Floating point MAC (~thousands)
Connected by mesh of programmable wires
Sitting inside a ring of high-speed I/O
With an optional embedded processor
Common within infrastructure hardware
Can buy on PCIe cards ready to go today
Lookup
tables
Numerics/
DSPs
RAMs

## Slide 10: FPGA Value
Spatial architecture – many data flow algorithms map well
  Data dependences across parallel work
  Streaming and graph processing patterns
  Enables some algorithms, makes others tractable to express
Rich I/O
  Network, memory, custom interfaces and protocols
  Very low + deterministic latencies
Large distributed on-chip memory BW
  Custom topologies tuned to algorithm

## Slide 11: Development Flows
Compile times to hardware longer than SW developers are used to
  Tools + reporting allow most development to be done without HW compilation

## Slide 12: Deep Spatial Pipelines: Creating Parallelism
h.parallel_for({8,8,8}, [=](auto I) {
output[I] = in[I] * 5;
});
h.single_task([=] {
for (int i=2; i < size; i++) {
A[i] = A[i-1] * foo(A[i-2]); …;
} });
Loop:
ND-range:

## Slide 13: One FPGA-Specific Language Feature (of many)
Data flow pipes:
constexpr int count = 1024; using my_pipe = pipe<class some_pipe, int>;
std::array<int, count> in_array;
for (int i=0; i < count; i++) { in_array[i] = i;} // Init
buffer B_in{ in_array }; // Init from std::array
buffer<int> B_out{ range{count} }; queue Q{ INTEL::fpga_emulator_selector{} };
// ND-range kernel
Q.submit([&](handler& h) {
auto A = accessor(B_in, h);
h.parallel_for(count, [=](auto idx) {
my_pipe::write( A[idx] );
}); });
// Single_task kernel
Q.submit([&](handler& h) {
auto A = accessor(B_out, h);
h.single_task([=]() {
for (int i=0; i < count; i++) {
A[i] = my_pipe::read();
}
}); });
Combine task graph abstraction with data flow